## Slide 1: ANTERPOLATOR
Estimation of spatial values based on
Ant Colony Optimization
Roberto Aguirre Maturana
Geologist – Universidad de Chile
rhaguirrem@gmail.com

## Slide 2: ANTERPOLATOR
Numeric interpolator based on Ant Colony Optimization (ACO).
The input is a set of samples with known coordinates
volume occupied by cells is divided by a regular grid with cells of user-defined size.
Each grid cell has 26 neighbor cells, except for cells in the boundaries of the volume.
Each cell with samples has a value assigned equal to the average value of the cells it contains. Cells without samples have no default value assigned.
A number of ants is generated. Each ant has a random starting position corresponding to some of the cells with samples.
Ants generate a prediction for the value of their current cell, as a weighted average value of each neighbor cell.
The prediction is assigned to the current cell (unless it’s a cell with samples).
Options for cell value assignment: If current cell already has a value, it’s replaced by prediction or averaged with prediction. If current cell has no value, either it’s replaced by prediction or averaged with a background value defined by user. In both cases average value has a weight, also user-defined.
After assignment, cells move to a neighbor cell. A cell is considered prioritary if it hasn’t been visited yet by any ant, has no samples or if it’s value is closer to the value of the current cell according to some user-defined tolerance. In case there are no prioritary cells, a random neighbor is chosen.

## Slide 3
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 848558 (97.50%)
This result was obtained before adding the condition of neighbor cells with first priority for visit not including cells with samples. Notice the isolated drillhole section at the center.

## Slide 4
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 809246 (92.98%)
After adding the condition of neighbor cells with first priority for visiting not including cells with samples, continuity of the isogrades increased.

## Slide 5
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Visit decay lambda: 8
Background value for None cells: False
Cells visited: 808125 (92.85%)

## Slide 6
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.75
Background Value for None Cells: False
Cells visited: 801554 (92.10%)
After adding the condition of neighbor cells with first priority for visiting not including cells with samples, continuity of the isogrades increased.

## Slide 7
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.9
Background Value for None Cells: False
Cells visited: 804983 (92.49%)
After adding the condition of neighbor cells with first priority for visiting not including cells with samples, continuity of the isogrades increased.

## Slide 8
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 1 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Decay rate: 64
Background value for None cells: False
Cells visited: 836803 (96.15%)
A neighbor cell value is considered close to a cell is the absolute difference between their values is lesser than a threshold defined by the product of the class size and the tolerance. A smaller class size restricts the neighbor cells considered first priority for ant moving.

## Slide 9
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 1 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: None
Decay rate: 1024
Background value for None cells: False
Cells visited: 828246 (95.16%)
The new value of a cell is a weighted average of the predicted value and the current value of the cell. One option is to calculate the weight as a function of the distance to the nearest sample.
pw: predicted weight
dr: decay rate
nsd: distance to nearest sample
New value = pw x predicted + (1 – pw) x current

## Slide 10
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.9
Visit decay lambda: 4
Background value for None cells: False
Cells visited: 797095 (91.58%)
Visit decay lambda purpose is to control how fast the interpolated values converge to background away from samples. Instead of a distance function it’s based on number of visits on each cell.

## Slide 11
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.9
Visit decay lambda: 8
Background value for None cells: False
Cells visited: 818279 (94.02%)
Visit decay lambda doesn’t give enough continuity to close samples, even when values are high enough as to excessively extend the interpolation into areas away from samples.

## Slide 12
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Decay rate: 0.1
Background value for None cells: False
Cells visited: 792945 (91.11%)
Decay rate controls the influence of distance to samples in the convergence of the interpolation to background value.

## Slide 13
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Decay rate: 2
Background value for None cells: False
Cells visited: 800446 (91.97%)
Decay rate controls the influence of distance to samples in the convergence of the interpolation to background value.

## Slide 14
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Decay rate: 2
Background value for None cells: False
Cells visited: 800446 (91.97%)
Decay rate controls the influence of distance to samples in the convergence of the interpolation to background value.

## Slide 15
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: True
Cells visited: 786610 (90.38%)
Assuming the background value for first time visited blank cells when averaging with ant prediction based on neighbors makes for a very conservative interpolation.

## Slide 16
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.3
Background Value for None Cells: True
Cells visited: 785662 (90.27%)

## Slide 17
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.1
Background Value for None Cells: True
Cells visited: 795747 (91.43%)
Reducing the cell weight when averaging it with predictions makes for a less conservative estimation, even when background value is assumed for blank cells.

## Slide 18
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.01
Background Value for None Cells: True
Cells visited: 795975 (91.45%)
Reducing the cell weight when averaging it with predictions makes for a less conservative estimation, even when background value is assumed for blank cells.

## Slide 19
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0
Background Value for None Cells: True
Cells visited: 803787 (92.35%)
A cell weight of 0 seems to be essentially the same as not using the cell value on the interpolation.

## Slide 20
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 1 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Decay rate: 10
Background value for None cells: False
Cells visited: 841662 (96.70%)
The prediction of a cell value is calculated as a weighted average of the values of the neighbor cells. In this example the weight used is the distance to the nearest sample.

## Slide 21
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 1 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.25
Decay rate: 10
Background value for None cells: False
Cells visited: 838289 (96.32%)
The prediction of a cell value is calculated as a weighted average of the values of the neighbor cells. In this example the weight used is the distance to the nearest sample.

## Slide 22
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Sample distance range: 10
Background value: 0
Iterations: 1000
Cell weight: 0.5 - Decay rate: None
Background value for None cells: False
Cells visited: 458630 (52.70%)
Sample distance range is a parameter that prioritizes moving to cells within a user-defined distance from cells with samples. In this example it was defined as the only first priority parameter. The result is ants remaining closer to samples.

## Slide 23
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Sample distance range: 5
Background value: 0
Iterations: 1000
Cell weight for post prediction averaging: 0.5 - Decay rate: None
Probability of including cell value during prediction: 1
Background value for None cells: True
Cells visited: 784204 (90.10%)

## Slide 24
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Sample distance range: 5
Background value: 0
Iterations: 500
Cell weight for post prediction averaging: None - Decay rate: None
Probability of including cell value during prediction: 0
Background value for None cells: False
Cells visited: 804652 (92.45%)

## Slide 25
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Sample distance range: 5
Background value: 0
Iterations: 1000
Cell weight for post prediction averaging: None - Decay rate: None
Probability of including cell value during prediction: 0
Background value for None cells: True
Cells visited: 800534 (91.98%)

## Slide 26
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Sample distance range: 5
Background value: 0
Iterations: 200
Cell weight for post prediction averaging: None - Decay rate: None
Probability of including cell value during prediction: 0
Background value for None cells: False
Cells visited: 632218 (72.64%)
Result after registering for each visited cell the closest sample and using this value for weight calculation during prediction. Less difference between the value of the last visited cell and the cell value of a neighbor cell makes for a biggest weight of that neighbor on interpolation.

## Slide 27
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 2 - Tolerance: 1
Sample distance range: 10
Background value: 0
Iterations: 200
Decay rate: None
Probability of including cell value during prediction: 0
Background value for None cells: True
Fill unvisited cells with neighbors average: True
Cells visited: 665928 (76.51%)
Sample distance range is a parameter used to control the extension of the anomaly by assuming background value for None cells beyond a certain distance form the nearest cell with samples. Non-visited cells were filled using the average value of their neighbors.

## Slide 28
Samples: 27414
Cell Size: 20x20x20
Total cells: 110577
Cells with samples: 2974
Starting ants: 8922 - Surviving ants: 8922
Max pheromone: 150
Class size: 2 - Tolerance: 1
Domain average distance: 7 - Background distance: 10
Background value: 0
Decay rate: 1
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_sample
Fill unvisited cells with neighbors average: False
Iterations: 20
Cells visited: 78125 (70.65%)

## Slide 29
Samples: 27414
Cell Size: 20x20x20
Total cells: 110577
Cells with samples: 2974
Starting ants: 8922 - Surviving ants: 8922
Max pheromone: 150
Class size: 2 - Tolerance: 1
Domain average distance: 7 - Background distance: 10
Background value: 0
Decay rate: 1
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_sample
Fill unvisited cells with neighbors average: False
Iterations: 10
Cells visited: 63549 (57.47%)

## Slide 30
Samples: 27414
Cell Size: 20x20x20
Total cells: 110577
Cells with samples: 2974
Starting ants: 8922 - Surviving ants: 8922
Max pheromone: 150
Class size: 2 - Tolerance: 1
Domain average distance: 7 - Background distance: 10
Background value: 0
Decay rate: 0.5
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_sample
Fill unvisited cells with neighbors average: False
Iterations: 10
Cells visited: 63845 (57.74%)

## Slide 31
In this example a fault divides de boundary in two domains. In this case, the criteria for priority considers that the direction from current cell to neighbor is the same as the direction from last cell to current, and neighbor cell sharing the same mark of class. weight is based on cell value, Greater value means greater wieight.
Samples: 468
Cell Size: 25x25x25
Total cells: 229320
Cells with samples: 241
Ants: 723
Class size: 0.2 - Tolerance: 1
Domain average distance: 100 - Background distance: 10
Background value: 0
Decay rate: 2
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_value
Fill unvisited cells with neighbors average: False
Iterations: 200
Cells visited: 188276 (82.10%)

## Slide 32
In this example a fault divides de boundary in two domains. In this case, the criteria for priority considers that the direction from current cell to neighbor is the same as the direction from last cell to current, and neighbor cell sharing the same mark of class. weight is based on cell value, Greater value means greater wieight.
Samples: 468
Cell Size: 25x25x25
Total cells: 229320
Cells with samples: 241
Ants: 723
Class size: 0.2 - Tolerance: 1
Domain average distance: 100 - Background distance: 10
Background value: 0
Decay rate: 0.5
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_value
Fill unvisited cells with neighbors average: False
Iterations: 200
Cells visited: 187348 (81.70%)

## Slide 33
In this example a fault divides de boundary in two domains. In this case, the criteria for priority considers that the direction from current cell to neighbor is the same as the direction from last cell to current, and neighbor cell sharing the same mark of class. Weight is based on nearest sample. The closer to a sample means the greater the weight.
Samples: 468
Cell Size: 25x25x25
Total cells: 229320
Cells with samples: 241
Ants: 723
Class size: 0.2 - Tolerance: 1
Domain average distance: 100 - Background distance: 10
Background value: 0
Decay rate: 2
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: nearest_sample
Fill unvisited cells with neighbors average: False
Iterations: 200
Cells visited: 188276 (82.10%)

## Slide 34
In this example a fault divides de boundary in two domains. Weight is based on value of the closest sample. The greater the value of the closest sample the greater the weight.
Samples: 468
Cell Size: 25x25x25
Total cells: 229320
Cells with samples: 241
Ants: 723
Class size: 0.2 - Tolerance: 1
Domain average distance: 7 - Background distance: 10
Background value: 0
Decay rate: 1.5
Probability of including cell value during prediction: 0
Value for None cells: True
Weight method: greater_sample
Fill unvisited cells with neighbors average: False
Iterations: 200
Cells visited: 224511 (82.93%)

## Slide 35
Samples: 21908
Cell Size: 5x5x5
Total cells: 3726450
Cells with samples: 1077347
Ants: 3000
Class size: 1 - Tolerance: 1
Sample distance range: 10
Background value: 0
Decay rate: 0.5
Probability of including cell value during prediction: 0
Background value for None cells: True
Fill unvisited cells with neighbors average: False
Iterations: 500
Cells visited: 1301637 (34.93%)
Domained estimation.
Currently, the formula for weighting of neighbor cells is:
fValue = get_mark_of_class(abs(last_cell.closest_sample - cell.value), self.class_size)
weight = self.class_size/(self.class_size + fValue ** self.decay_rate)

## Slide 36
Anterpolator
Kriging

## Slide 37
Samples: 21908
Cell Size: 5x5x5
Total cells: 3726450
Cells with samples: 1077347
Ants: 3000
Class size: 1 - Tolerance: 1
Sample distance range: 10
Background value: 0
Decay rate: 0.5
Probability of including cell value during prediction: 0
Background value for None cells: True
Fill unvisited cells with neighbors average: False
Iterations: 500
Cells visited: 1301637 (34.93%)
Comparison of Anterpolator and Kriging

## Slide 38
Samples: 21908
Cell Size: 5x5x5
Total cells: 3726450
Cells with samples: 1077347
Ants: 3000
Class size: 1 - Tolerance: 1
Sample distance range: 10
Background value: 0
Decay rate: 0.5
Probability of including cell value during prediction: 0
Background value for None cells: True
Fill unvisited cells with neighbors average: False
Iterations: 500
Cells visited: 1301637 (34.93%)
Comparison of Anterpolator and Kriging

## Slide 39
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 500
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 720366 (82.77%)

## Slide 40
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 20000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 250
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 613422 (70.48%)

## Slide 41
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0
Background Value for None Cells: False
Cells visited: 849198 (97.57%)

## Slide 42
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 200
Cell weight: 0
Background Value for None Cells: False
Cells visited: 461938 (53.08%)

## Slide 43
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 848558 (97.50%)

## Slide 44
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 809246 (92.98%)

## Slide 45
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 500
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 720366 (82.77%)

## Slide 46
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 20000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 100
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 394875 (45.37%)

## Slide 47
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0
Background Value for None Cells: False
Cells visited: 849198 (97.57%)

## Slide 48
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 200
Cell weight: 0
Background Value for None Cells: False
Cells visited: 461938 (53.08%)

## Slide 49
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 10000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 848558 (97.50%)

## Slide 50
Samples: 27414
Cell Size: 10x10x10
Total cells: 870348
Cells with samples: 6119
Ants: 5000
Class size: 5 - Tolerance: 1
Background value: 0
Iterations: 1000
Cell weight: 0.5
Background Value for None Cells: False
Cells visited: 809246 (92.98%)